1) The total resistance of system is (Ω is an Om sign.):

a) 6.4 kΩ
b) 4.8 kΩ
c) 4.0 kΩ
d) 5.6 kΩ

2) Choose the right word to the place of three dots (...):

 are both conductors and resistors under certain conditions

a) Conductors
b) Semiconductors
c) Insultors

3) XOR gate produces true:

a) when all inputs are only 0.
b) when all inputs are only 1.
c) when all inputs are 0 and 1.
d) only when odd number of inputs are 1.

Different

4) Choose the right statements coming from Ohm’s Law:

1) a Current varies directly with a voltage;
2) a Current varies inversely with a voltage;
3) a Current varies directly with a resistance;
4) a Current varies inversely with a resistance;
5) a Resistance varies directly with a voltage;
6) a Resistance varies inversely with a current;

a) 1, 4, 5, 6;
b) 2, 3
c) 1, 4

5) Choose the right words to the place of three dots (...):

… is the only register connected to the data bus, and all data should go through this register.

a) Memory Address Register (MAR).
b) Memory Buffer Register (MBR).
c) Instruction Register (IR).
d) Program Counter (PC).

6) Choose the right words to the place of three dots (...):

the address of next instruction in the program counter (PU) is placed there initially by ... and updated automatically by ...:

a) the operation system, the CPU.
b) the CPU, the operation system.
c) memory address registers, memory buffer registers.

7) Choose the right word to the place of three dots (...):

… is the only register connected to the address bus, and all addresses should go through this register.

a) Memory Address Register (MAR).
b) Memory Buffer Register (MBR).
c) Instruction Register (IR).
d) Program Counter (PC).

8) Choose the right words to the place of three dots (...):

Add Immediate (AI) command differs from Add (A) with that an operand … :

a) is a content of memory pointed to be added to an accumulator.
b) is what is added to an accumulator.
c) is a content of memory pointed to be added to a storage.
d) is what is added to a storage.

9) Choose the right order of thin instruction cycle:

a) Fetch – Decode – Execute
b) Decode – Fetch – Execute
c) Execute – Fetch – Decode
c) Execute – Decode – Fetch

10) Choose the right words to the place of three dots (...):

The number of ... assigned to the opcode will determine the ... number of ... that processor is allowed to have.

a) operands, maximum, operators.
b) bits, minimum, instructions.
c) bits, maximum, instructions.
d) operators, average, storage.

Answers

1) c
2) b
3) d
4) c
5) b
6) a
7) a
8) b
9) a
10) c